## Slide 1: Two models, two public casting datasets
Both look at photos of cast aluminium parts. Each one answers a different question.
1
Defect model
YOLO11s finds, names and boxes each defect
1,769
labelled photos, every defect marked with a box
Dataset casting_dataset_kaggle, Roboflow, CC BY 4.0
Split 1,239 train · 356 validation · 174 test
Defects crack, scratch, blowholes, shrinkage, flash, scar, misrun, cold shot
Result mAP50 0.75 on unseen test photos (crack 0.93)
Source: universe.roboflow.com/detect-casting-defect
2
Anomaly model
PatchCore learns what a good part looks like
2,875
good parts only, no labels needed
Dataset Casting product image data for quality inspection, Kaggle
Full set 7,348 pump impeller photos; we used all 2,875 good ones
Test 524 parts (262 good, 262 defective)
Result AUROC 0.96, F1 0.88, with a heat-map of the fault
Source: kaggle.com/datasets/ravirajsinh45 (Ravirajsinh Dabhi)
Notes: Two models, two datasets. The defect model is YOLO11s, trained on 1,769 labelled photos from the Roboflow Universe dataset casting_dataset_kaggle (CC BY 4.0). Every defect is marked with a box, across 8 types. On 174 test photos it never saw it scores mAP50 0.75, and 0.93 on cracks. The anomaly model is PatchCore. It only needs good parts: we gave it all 2,875 good pump impeller photos from the Kaggle casting product dataset (7,348 photos in total). On 524 test parts it reaches AUROC 0.96 and F1 0.88, and it draws a heat-map of anything unusual, even defect types it was never shown. Honest caveat if asked: the Roboflow set likely has near-duplicate copies across train and test, so 0.75 is somewhat optimistic.